## Slide 1
Open AGV_UI in VNC Viewer (PC) on myAGV
Be patient, it takes a while...

## Slide 2
First, turn on LIDAR.
A message appears in this window: “Radar open.”
A window opens in the background from ROS, providing information about the LIDAR function. The window can be closed by clicking on the “Close” button.

## Slide 3
Now switch on the control via keyboard. Press the “Start” button.
The ROS window in the background displays information on controlling the AGV (for more details, see also the GitBook).

## Slide 4
Use the control buttons (or alternatively, the gamepad without a keyboard) to move the myAGV slightly back and forth.
The LIDAR sensor is already recording the room.

## Slide 5
Now, click on Open Build Map. RViz opens, and the already captured environment is displayed(see next slide).

## Slide 7
With 3D Navigation and Navigation, you can create maps just like before with Rviz.
Further functionality, then according to Gitbook (Prof. Dr Sommer has the documents)